## Slide 1
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review III
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Arjun V P
T9987
VIT Chennai
Knowledge partner | Implementation partner

## Slide 2
Industrial rotating machinery is highly dependent on the reliable operation of rolling-element bearings.
Bearing faults can cause unexpected machine downtime, reduced efficiency, increased maintenance costs, and potential equipment failure.
Vibration analysis is a widely used technique for detecting and identifying bearing health conditions.
Traditional AI-based diagnostic systems may produce probabilistic predictions, making their reasoning difficult to validate and reproduce consistently.
This project proposes a Deterministic MCP (Model Context Protocol)-Driven AI Agent for reliable and explainable ball bearing fault diagnosis.
The system uses the NASA Bearing Dataset as the primary source of vibration data for developing and evaluating the diagnostic approach.
Introduction
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics

## Slide 3
To develop a Deterministic MCP-Driven AI Agent for ball bearing health monitoring and fault diagnosis.
To analyze vibration signals and accurately identify different bearing health conditions.
To incorporate ISO-based standards and diagnostic principles into the analysis workflow.
To provide consistent, explainable, and reproducible fault identification rather than relying solely on probabilistic outputs.
To assist maintenance engineers and reliability teams in making informed maintenance decisions.
To reduce the risk of unplanned equipment failures, downtime, and unnecessary maintenance.
Objective
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics

## Slide 4
Modules to cover
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
4. Deterministic Diagnostic Engine
Rule/threshold-based decision logic
Consistent and reproducible diagnosis
ISO-based diagnostic criteria
5. MCP-Driven AI Agent
MCP tools and structured context
Agent-based diagnostic workflow
Explainable reasoning and fault identification
6. Results & Validation
Bearing fault classification
Diagnostic explanation
Accuracy and consistency evaluation

## Slide 5
Unplanned bearing failures can lead to equipment downtime, maintenance costs, and reduced operational reliability.
Traditional maintenance approaches often rely on fixed schedules or manual inspection, which may miss progressive bearing degradation.
Vibration data contains important indicators of bearing health and degradation, but raw telemetry is difficult for engineers to interpret continuously.
Existing predictive models can provide individual predictions, but often lack an interactive decision-support layer that connects diagnostics, trends, and maintenance actions.
Therefore, there is a need for a system that can analyze historical vibration telemetry, assess bearing degradation, compare assets, and assist engineers in making evidence-based maintenance decisions.
Problem Statement
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics

## Slide 6
Python Modules
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
RAW VIBRATION DATA
↓
data.py → features.py → build_features.py
↓
observations.py
↓
health.py → rul.py / rul_model.py
↓
api.py
↓
mcp_server.py
↓
agent.py
↓
Maintenance Decision Support

## Slide 7
Data & Feature Processing
data.py — Dataset ingestion, validation, file discovery and timestamp parsing
features.py — Extracts RMS, Kurtosis, Peak-to-Peak and Crest Factor
build_features.py — Processes raw vibration files into structured feature data
observations.py — Converts feature data into bearing-level observations
Health & Prognostics
health.py — Baseline deviation, degradation index and health score calculation
rul.py — Generates Remaining Useful Life (RUL) targets
rul_model.py — XGBoost-based baseline RUL model and evaluation
Python Modules
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Application & Agentic Layer
api.py — FastAPI backend for telemetry, historical snapshots and agent requests
mcp_server.py — Exposes health, trend, maintenance and bearing-comparison tools through MCP
agent.py — Llama 3.2 agent for tool orchestration and maintenance-oriented interpretation
Supporting
__init__.py — Python package initialization

## Slide 8
Approach/Algorithms/Tools
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Algorithms & Approach
Vibration Feature Extraction: RMS, Kurtosis, Peak-to-Peak, Crest Factor
Health Assessment: Healthy baseline → feature deviation → robust scaling → rolling-median smoothing
Degradation Index: Quantifies deviation from normal bearing behavior
Health Score: Converts degradation into a bounded 0–100 health indicator
Trend Analysis: Recent degradation and health-score slope
RUL Baseline: XGBoost regression evaluated as an initial prognostic baseline
Agentic Decision Support: MCP tools provide deterministic diagnostics; Llama 3.2 selects/interprets tool outputs
Tools & Technologies
Python: NumPy, Pandas, SciPy, scikit-learn
ML: XGBoost, Joblib
Backend: FastAPI, Uvicorn
Agentic AI: MCP, Ollama, Llama 3.2
Frontend: HTML, CSS, JavaScript, Chart.js
Data: NASA IMS Run-to-Failure Bearing Dataset
Development: VS Code, Git/GitHub

## Slide 9
Processed 984 NASA IMS observations across 4 bearings and extracted key vibration features.
Developed baseline-relative degradation and health scoring, revealing increasing degradation toward end-of-run.
At the final observation, Bearing 1 had the highest degradation (73.28) and lowest health score (0.01/100).
MCP-based diagnostics successfully provide health, trend, maintenance recommendation, and bearing comparison.
Llama 3.2 + MCP successfully converts deterministic diagnostic results into engineer-facing maintenance insights.
Initial XGBoost RUL baseline was not sufficiently reliable, highlighting the need for trajectory-based prognostics.
Findings and Results
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics

## Slide 10
Developed an end-to-end predictive maintenance prototype for bearing vibration monitoring using NASA IMS run-to-failure data.
Combined feature extraction, health/degradation assessment, historical trend analysis, and MCP-based diagnostics into a single workflow.
The agentic layer enables Llama 3.2 to interpret deterministic engineering results and provide maintenance-oriented insights.
The system successfully identifies high-priority bearings and supports evidence-based maintenance decisions through an interactive dashboard.
The initial RUL model highlighted the importance of trajectory-based prognostics, providing a clear direction for future improvement.
Overall, the project demonstrates how deterministic signal analytics + MCP + local LLM orchestration can form a practical decision-support system for predictive maintenance.
Conclusion
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics

## Slide 12
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review III
Edge-Optimized RAG and Localized Failure Mitigation for Automated Assembly Lines Using Quantized SLM
Arjun V P
T9987
VIT Chennai
Knowledge partner | Implementation partner

## Slide 13
Automated assembly lines require rapid and reliable failure diagnosis to minimize downtime.
Machine failures can reduce production efficiency, equipment availability, and operational reliability.
Cloud-based AI solutions may introduce latency, connectivity, and data-dependency constraints.
Large AI models can also be resource-intensive for edge deployment.
This project proposes an Edge-Optimized RAG system to provide localized, knowledge-grounded failure diagnosis.
The system aims to assist operators with real-time failure identification and mitigation recommendations.
Introduction
Edge-Optimized RAG and Localized Failure Mitigation

## Slide 14
To develop an Edge-Optimized Retrieval-Augmented Generation (RAG) system for machine failure diagnosis.
To use a Quantized Small Language Model (SLM) suitable for resource-constrained edge devices.
To retrieve relevant failure knowledge and maintenance information from a local knowledge base.
To provide localized mitigation recommendations based on the identified failure.
To minimize latency, computational requirements, and dependence on cloud connectivity.
To support maintenance operators and production engineers in real-time decision-making.
Objective
Edge-Optimized RAG and Localized Failure Mitigation

## Slide 15
Modules to cover
Edge-Optimized RAG and Localized Failure Mitigation
4. Retrieval System Query → relevant failure knowledge
↓
5. Quantized SLM Retrieved context → grounded response
↓
6. Edge Deployment Low-latency diagnosis → localized mitigation recommendation
Machine Data → Failure Detection → Knowledge Retrieval → Quantized SLM → Diagnosis + Mitigation
1. Data Preparation AI4I dataset → cleaning → preprocessing
↓
2. Failure Classification Healthy / HDF / PWF / OSF / TWF / RNF
↓
3. Knowledge Base Failure descriptions → causes → maintenance procedures

## Slide 16
Industrial machines generate continuous telemetry, but identifying when a machine is approaching failure and what action to take remains challenging.
Predictive ML models can detect likely failures, but often do not provide context-aware maintenance guidance.
Maintenance engineers must manually search through SOPs, diagnostic procedures, safety instructions, and maintenance documents.
Cloud-based LLM solutions can introduce latency, connectivity, privacy, and deployment constraints in industrial environments.
EdgeRAG aims to bridge this gap by combining predictive maintenance, local RAG, and an SLM to transform machine telemetry into an evidence-grounded maintenance report locally at the edge.
Problem Statement
Edge-Optimized RAG and Localized Failure Mitigation

## Slide 17
DATA & MODELING
validation.py → dataset quality and label consistency checks
train.py → machine-failure and fault-mode model training
predictor.py → failure prediction and fault probabilities
thresholds.py → F2-based decision threshold selection
INGESTION
loader.py → document loading and metadata extraction
splitter.py → recursive document chunking
indexer.py → embeddings and Chroma vector indexing
ingest.py → end-to-end knowledge-base ingestion
Python Modules
Edge-Optimized RAG and Localized Failure Mitigation
RETRIEVAL & PIPELINE
machine_condition.py → ML output to structured machine condition retriever.py → semantic retrieval, fault-aware reranking and source diversification
GENERATION & APPLICATION
generator.py → local SLM-based maintenance report generation main.py → FastAPI backend and API endpoints config.yaml → configurable models, chunking and retrieval settings

## Slide 18
Approach/Algorithms/Tools
Edge-Optimized RAG and Localized Failure Mitigation
Component | Approach / Algorithm | Tools
Data Processing | Validation, cleaning & feature preparation | Pandas, NumPy
Failure Prediction | Random Forest classifier | Scikit-learn
Fault Diagnosis | One-vs-Rest classification + F2 threshold tuning | Scikit-learn
RAG Ingestion | Recursive chunking + metadata extraction | LangChain
Embeddings | Local text embeddings | Ollama – nomic-embed-text
Retrieval | Semantic similarity + fault-aware reranking | Chroma + LangChain
Generation | Evidence-grounded maintenance report | Ollama – Local SLM
Application | Local REST API + dashboard | FastAPI, HTML/CSS/JavaScript

## Slide 19
Random Forest successfully predicts machine failure, achieving a test ROC-AUC of approximately 0.97.
Fault-specific diagnosis was achieved for major failure modes such as HDF, PWF and OSF, with threshold tuning used to prioritize failure recall.
Metadata-aware RAG retrieval improved fault relevance compared with semantic-only retrieval, placing the relevant failure SOP and supporting maintenance documents among the top results.
The local SLM generates maintenance incident reports grounded in retrieved industrial knowledge, including diagnostic assessment, actions, escalation and restart guidance.
The system operates locally using Ollama, Chroma and FastAPI, avoiding dependence on cloud inference during operation.
TWF prediction and SLM grounding remain limitations, highlighting areas for further model and evaluation refinement.
Findings and Results
Edge-Optimized RAG and Localized Failure Mitigation

## Slide 20
EdgeRAG successfully integrates predictive maintenance, RAG and local SLM generation into a single end-to-end system.
Machine telemetry is transformed into failure predictions and fault diagnoses, which guide retrieval of relevant maintenance knowledge.
Chroma-based local RAG provides supporting SOPs, diagnostic procedures and maintenance guidance to the generation layer.
A local SLM through Ollama converts the retrieved evidence and machine condition into an actionable maintenance report.
The local-first architecture demonstrates the feasibility of privacy-preserving, low-dependency AI assistance for edge industrial environments.
The project establishes a practical foundation for future improvements in model efficiency, retrieval evaluation, SLM grounding and edge deployment performance.
Conclusion
Edge-Optimized RAG and Localized Failure Mitigation

## Slide 22
Calibri body 28
Acknowledgement … Calibri body -36
Project Title - Calibri body 18

## Slide 23
Calibri body 28
Reference… Calibri body -36
Project Title - Calibri body 18